## Slide 1: Unit 5, Lesson 13 Storage Technologies and Devices
AOIT Computer Systems
Copyright © 2008–2013 National Academy Foundation. All rights reserved.

## Slide 2: Three technologies are commonly used for storing data
Magnetic storage
  Hard drives for primary storage
  Tape drives for archiving large amounts of data
Flash storage
  SSDs (solid-state drives) for primary storage on newer PCs
  Thumb drives used as portable storage
  Flash cards (sometimes called flash memory) commonly used in digital cameras
Optical storage
  CDs
  DVDs

## Slide 3: Magnetic storage includes hard drives and tape drives
Hard drives use sophisticated magnetic recording and playback technologies.
Tape drives are used to store archives.
Advantages include:
  Easy to read, write, and erase
  Low cost
  Easy to store cartridges for safekeeping
What do you think would happen if you put a magnet inside a hard drive?
Magnetic Storage

## Slide 4: Computers store data electronically
Hard drives use magnetization to record data on platters.
Hard drives are electromechanical because they have moving parts but are controlled by electricity.
Why do you think a hard drive must remain sealed?
Magnetic Storage

## Slide 5: Most hard drives have multiple platters and read/write heads
A typical hard drive consists of a spindle holding one or more double-sided platters.
Each magnetic platter surface on the spindle is accessed by one head.
The heads are on an arm called an actuator that holds them over the platters.
Magnetic Storage
How many platters does this hard drive have? How many read/write heads?

## Slide 6: Hard drives use a standards-based interface to communicate with the system bus
The standards determine the performance characteristics of the drive, such as bandwidth and data transfer speeds.
Newer hard drives have integrated controllers mounted on the base of the drive that control data transfers.
  Most newer hard drives use serial attached SCSI (SAS) or serial ATA (SATA) standards.
Magnetic Storage

## Slide 7: Use error-checking and defragmentation utilities to maintain a hard drive
Scandisk checks a hard drive for data errors.
Disk Defragmenter consolidates fragmented files on a hard disk to improve performance.
Magnetic Storage

## Slide 8: External hard drives are used for backup, transport, and extra storage space
They are a simple and inexpensive way to add extra hard drive storage space or provide backup of important files.
The removable, self-contained unit connects to a PC through a USB or FireWire port.
The drive mechanism and the media are in one sealed case.
Three models of external hard drives
Magnetic Storage
Notes: Image retrieved from http://en.wikipedia.org/wiki/File:External_hard_drives.jpg on June 19, 2012, and reproduced here under the terms of the Creative Commons Attribution-Share Alike 3.0 Unported license. Image courtesy of TonyTheTiger.

## Slide 9: Tape drives store data on magnetic tapes
Have you ever played a cassette tape or a video cassette?
Read/write heads for tape are stationary, unlike the fast-moving heads of a hard drive.
Unlike hard drives that find data quickly, tapes require fast-forwarding or rewinding to find data.
Tapes are cost-effective and stable.
Tapes are typically used for archiving data from hard drives.
Tapes can be erased and reused many times.
Magnetic Storage

## Slide 10: The performance of hard drives and tape drives is measured in a similar way
Magnetic Storage
Data rate | The number of bytes per second that the device delivers to the processor
Seek time | The time it takes for the head to move to the right place to read or write data
Capacity | How many bytes of data the device can hold

## Slide 11: Two kinds of magnetic storage serve two purposes
  Hard drives provide quick access.
  Tape drives are good for long-term storage of data that is not accessed as frequently.
  Tapes are easy to store off-site.
Magnetic Storage

## Slide 12: Solid-state drives (SSDs) use flash technology
Solid state means that everything is electronic instead of mechanical. There are no moving parts.
  Flash storage technology involves storing data on interconnected flash memory chips. These are integrated circuit assemblies.
The flash technology retains data when the power is turned off.
Like all flash storage devices, SSDs can be erased and reprogrammed.
Flash Storage

## Slide 13: SSDs are replacing hard drives in newer computers
Hard drive Solid-state device
  An SSD is designed to reside inside the computer in place of a hard drive.
    SSDs share common I/O interface technology with hard drives.
    SSHDs (hybrid solid-state drives) combine a hard drive and an SSD drive
Flash Storage
Notes: Image retrieved from http://commons.wikimedia.org/wiki/File:Disassembled_HDD_and_SSD.JPG on January 28, 2013, and reproduced here under the terms of the Creative Commons Attribution-ShareAlike 2.5 Generic license (http://creativecommons.org/licenses/by-sa/2.5/deed.en). Image courtesy Rochellesinger.

## Slide 14: SSDs have several advantages over magnetic hard drives
Advantages of SSDs:
Less susceptible to physical shock
Silent
Faster seek time
Higher reliability
Less power usage
Lighter and smaller
Flash Storage

## Slide 15: Flash cards and thumb drives also use flash storage technology
Flash cards are designed for a specific target device, such as a digital camera or smartphone.
Thumb drives use flash technology and have a USB interface.
Flash memory in SSDs is faster and more reliable than the flash memory in thumb drives.
Flash Storage

## Slide 16: Optical storage technology uses light reflected from lasers
CDs and DVDs use optical storage technology to read and write data:
Data is stored in tiny indentations (pits) on a spiral track starting at the center of the CD. The flat areas between pits are called lands.
The read head emits a laser beam that reads a pit as a tiny raised bump. The bump reflects light differently than the flat lands.
A sensor that detects changes in light intensity reads the pits as 1 and the lands as 0.
Optical Storage

## Slide 17: Optical storage has advantages and disadvantages
Random data access is slower with optical storage:
Optical heads are larger and heavier than the read/write heads in a hard drive.
CDs and DVDs spin more slowly than hard drive platters.
Optical storage may be more reliable than magnetic storage because there is less wear and tear on the discs.
Optical Storage

## Slide 18: Storage technologies are different methods of reading and writing data
Magnetic storage | Record data magnetically on platters or tapes
Flash storage | Use integrated circuit assemblies to record data on memory chips
Optical storage | Use lasers to read data stored on discs with a reflective aluminum covering